## Slide 1: SB 743 CEQA Guidelines Update
Governor’s Office of Planning and Research

## Slide 2
Topics
What future do we want for California?
Issues with LOS in CEQA raised by stakeholders
What does SB 743 do?
New Primary Metric: Vehicle Miles Traveled
Draft CEQA Guidelines implementing SB 743
Models and technical considerations
Estimating the VMT effect of roadway expansion
Implementation Logistics

## Slide 3: Looking Forward…
Where will Californians
  Live?
  Work?
  Recreate?
Notes: Looking forward over the next few decades, when we are expected to reach 50 million people, we need to start asking where do we think people will live, work, etc.

## Slide 4: Growing Urban Footprint
Notes: Our historic growth pattern has been out.

## Slide 5
General Goal:
  Protect natural resources and improve quality of life by directing new growth to existing cities and suburbs

## Slide 6
  Analysis of infill development using LOS

## Slide 7
  Analysis of infill development using LOS
  Relatively little vehicle travel loaded onto the network

## Slide 8
  Analysis of infill development using LOS
  Relatively little vehicle travel loaded onto the network
  …but numerous LOS impacts

## Slide 9
  Analysis of greenfield development using LOS

## Slide 10
  Analysis of greenfield development using LOS
  Typically three to four times the vehicle travel loaded onto the network relative to infill development

## Slide 11
  Analysis of greenfield development using LOS
  Typically three to four times the vehicle travel loaded onto the network relative to infill development
  …but relatively few LOS impacts
  Traffic generated by the project is disperse enough by the time it reaches congested areas that it doesn’t trigger LOS thresholds, even though it contributes broadly to regional congestion.

## Slide 12: Problems with LOS
1. Bias against infill because of “last-in development” problem
  Infill loads relatively little traffic onto the regional network
  However, LOS methodology adds traffic generated by infill to existing traffic, triggering thresholds
2. Scale of analysis is too small
Registers impacts adjacent to project, ignores impacts regionally
Spot metric insufficient to show corridor/network impact/benefit

## Slide 13: Problems with LOS
3. LOS mitigation is itself problematic
Reducing project size pushes development to outlying locations
Widening roadways worsens livability, induces vehicle travel
4. Mischaracterizes transit, biking, walking as detriments to transportation
A transit priority lane worsens LOS even as it improves person-throughput
LOS characterizes pedestrians and cyclists as obstructions to cars, to be channeled/restricted
1 person
40 people
1 person
2 people

## Slide 14: Problems with LOS
5. LOS has a well-developed methodology, but is not more precise than other metrics
Trip distribution is difficult to predict accurately
LOS is sensitive to error in trip distribution
6. Delay-based metrics are problematic for modern transportation planning
The purpose of transportation is access to destinations
With smart growth, delay metrics sometimes get that backwards
From: CDM Smith, Traffic Forecast Guidelines for the 2010s
14

## Slide 15: Problems with LOS
7. LOS pushes us to build roads that we cannot afford to maintain
Substantial maintenance shortfalls even for existing roads
Maintaining LOS thresholds creates additional maintenance burden

## Slide 16: SB 743
Requires the Office of Planning and Research to develop new metrics for transportation impacts under CEQA

## Slide 17: SB 743 - Specifics
Requires a change in the status quo to be codified in the CEQA Guidelines
New metric required in transit areas at a minimum
LOS or delay may be used only if/where OPR specifies, otherwise no longer a CEQA impact
  Air, noise, safety impacts from transportation still CEQA impacts
Does not pre-empt local planning requirements, fee programs
OPR must specify criteria for a new metric, which must promote:
  Reduction in GHGs
  Development of multimodal transportation networks
  A diversity of land uses

## Slide 18
Other policy and administration goals
  Consistency with State Planning Priorities (Infill priority)
  General environmental benefit
  Improved Health
  Fiscal benefit
  Simplicity/feasibility
  Access to destinations
SB 743 - Objectives

## Slide 19
Vehicle Miles Traveled*
Automobile Trips Generated*
Multi-modal Level of Service
Fuel use
Vehicle Hours Traveled
Presumption of less than significant transportation impact based on location
* Recommended for consideration by the statute
Candidate Metrics

## Slide 20
Easier to model
  Many existing models
  Already calculating as part of estimating GHGs
Better accuracy
Captures full extent of vehicle travel
Mitigation doesn’t induce more vehicle travel
Mitigation forwards other environmental and human health factors
Consistent with a broad array of other goals, including fiscal health
Vehicle Miles Traveled

## Slide 21
VMT, Environment, Health, Cost
Environment
Emissions
  GHG
  Regional pollutants
Energy use
  Transportation energy
  Building energy
Water
  Water use
  Runoff – flooding
  Runoff – pollution
Consumption of open space
  Sensitive habitat
  Agricultural land
Health
Collisions
Physical activity
Emissions
  GHGs
  Regional pollutants
Mental health
Cost
Increased costs to state and local government
  Roads
  Other infrastructure
  Schools
  Services
Increased private cost
Housing supply/demand mismatch  future blight

## Slide 22
Primary Metric for CEQA Transportation Analysis: VMT
Continue to analyze impacts resulting from transportation
  Noise
  Air Quality
  Safety
Delay no longer an impact under CEQA
  “A project’s effect on automobile delay does not constitute a significant environmental impact”
Proposed Section 15064.3
743 Preliminary Draft CEQA Guidelines Update

## Slide 23
Old: LOS on local intersections and highway segments
New: VMT loaded onto the roadway network
  Possibly LTS if near transit
  Possibly LTS if reducing area-wide VMT
  Possibly significant if > regional average VMT (per capita, per employee, etc.)
  Methodology: deference to lead agency, rule of reason
Proposed Section 15064.3(b)(1)
Transportation Impacts of Land Use Projects

## Slide 24
Old: Transit, active transportation projects slow automobile traffic, trigger LOS “impact to transportation”
New: Transit, active transportation presumed to reduce VMT unless demonstrated otherwise
Proposed Section 15064.3(b)(2)
Transportation Impacts of Transit and Active Transport Projects

## Slide 25
Old: LOS impacts at nearby intersections from rerouted/induced vehicle travel
(Also: Induced VMT analysis required for GHG calculation)
New: Induced (or reduced) VMT
Proposed Section 15064.3(b)(2)
Transportation Impacts of Roadway Expansion Projects

## Slide 26
Safety
Potential safety issues
Increase exposure of cyclists and pedestrians (e.g. remove facilities, increase crossing distances)
Queues extending into the mainline
Speed differentials (<15 mph)
Increased motor vehicle speeds
Increased distance between bike or ped crossings
Proposed Section 15064.3(b)(3)

## Slide 27
Methodology
Deference to lead agencies
Rule of reason
May use models to estimate
May revise inputs/outputs to reflect professional judgment (explain assumptions)
Proposed Section 15064.3(b)(4)

## Slide 28
Mitigation and Alternatives
Examples proposed App F
Retains discretion for lead agencies
  Cities and Counties can still apply their general plan and zoning codes
Examples drawn from CAPCOA (peer-reviewed, quantifiable)
Previously adopted measures
Proposed Section 15064.3(c), Proposed additions to Appendix F

## Slide 29
Applicability
Phased approach to implementation
Guidelines apply prospectively only
Upon adoption, apply immediately within TPAs and HQTCs
Agencies can opt-in outside of those areas
Apply statewide after January 1, 2016
Proposed Section 15064.3(d)

## Slide 30: Models and Technical Considerations in Assessing Vehicle Miles Traveled

## Slide 31
Sketch models
  For land use projects & land use plans
  Approximately two dozen currently available, some free and downloadable
  Rapid improvement
Travel demand models
  For transportation projects & land use projects
  Recent state investment
Both used for GHG analyses for several years
Tools and Methods: Modeling VMT

## Slide 32
Trip-based calculation
  Residential: VMT/capita
  Office: VMT/employee
  Commercial or other: VMT/trip
  Alternative: VMT/person-trip
Area-wide calculation
  Change in VMT over the entire area
Tools and Methods: Counting VMT

## Slide 33
Methods for Counting VMT
CEQA Rule of Reason requires capturing spillover VMT

## Slide 34: Estimating VMT from Roadway Capacity Increasing Projects

## Slide 35
Causes
Empirical study
Estimating VMT increase
Roadway expansion projects typically increase VMT

## Slide 36
Roadway expansion reduces travel time, which leads to:
Longer trips
Mode shift toward automobile
Newly generated trips
Route changes (can ↑ or ↓ or VMT)
More disperse land use development
Causes

## Slide 37
1. Longer Trips (short-term)
Original VMT

## Slide 38
1. Longer Trips (short-term)
Original VMT
Added Capacity

## Slide 39
1. Longer Trips (short-term)
Original VMT
Additional VMT
Added Capacity

## Slide 40
1. Longer Trips (mid-term)

## Slide 41
1. Longer Trips (mid-term)

## Slide 42
2. Mode Shift

## Slide 43
2. Mode Shift

## Slide 44
3. Newly Generated Trips

## Slide 45
3. Newly Generated Trips

## Slide 46
4. Route Changes

## Slide 47
4. Route Changes

## Slide 48
5. Disperse Land Use

## Slide 49
5. Disperse Land Use

## Slide 50
5. Disperse Land Use

## Slide 51
30+ studies on induced vehicle travel
Long-run elasticities typically 0.6 to 1.0
Recent ARB assessment
  Policy Brief
  http://www.arb.ca.gov/cc/sb375/policies/hwycapacity/highway_capacity_brief-4-21-14.pdf
  Background Technical Document
  http://www.arb.ca.gov/cc/sb375/policies/hwycapacity/highway_capacity_bkgd-4-21-14.pdf
VMT effects extend beyond project
Empirical Study

## Slide 52
Empirical Study
Chart: Chart 2 - Long-Term Elasticity for All Improvement Types
| Cervero, Hansen, 2001 | Hansen, Huang, 1997 | Hansen, Huang, 1997 | Marshall, 1996 | Rodier, et.al., 2001 | Strathman, et.al., 2000 | Cervero, 2001 | Fulton, et.al., 2000 | Hansen et.al., 1993 | Noland, 2001 | Noland, 2001 | Noland, Cowart, 2000 | Cervero, 2002
 | 0.78 | 0.68 | 0.94 | 0.76 | 0.8 | 0.29 | 0.64 | 0.47 | 0.3 | 0.7 | 0.5 | 0.81 | 0.39
 | 0.06 | 0.01 | 0.01 | 0.09 | 0.3 | 0.01 | 0.01 | 0.42 | 0.3 | 0.3 | 0.3 | 0.19 | 0.01
Source: Fehr and Peers

## Slide 53
Estimation
A travel demand model can estimate:
Longer trips
Mode shift toward automobile
Newly generated trips [in some cases]
Route changes
But not:
Land use changes

## Slide 54
Estimation
Options for estimating land use changes:
Employ a land use model
Employ an expert panel, e.g. using Delphi method
Examine gap between modeled and typical empirical results; adjust and/or explain model results

## Slide 55
Implementation/Logistics
This is a preliminary discussion draft
  Share widely – input wanted - help with outreach appreciated
  Comment period through October 10
OPR incorporates comments, submits to Resources Agency
VMT goes live after formal rulemaking process
  Applies prospectively, not to in progress EIRs
  Initial application in TPAs, opt in elsewhere
  Statewide requirement January 1, 2016

## Slide 56: Thanks!
Chris Ganson
chris.ganson@opr.ca.gov

## Slide 57: Extra Slides

## Slide 58: VMT Mitigation Examples

## Slide 59: Land Use and Location
Increase densities
Increase location efficiency and destination accessibility
Increase diversity of development (mix uses)
Integrate affordable housing
Improve development design and connectivity
Locate close to existing bus or rail stations
Photo credit: Currey, G. (2013). Paseo de San Antonio II, San Jose [photograph].
Notes: This could be a good slide for a fruitvale photo

## Slide 60: Destination Facilities
Travel Demand Management programs:
  Ride-sharing, car-sharing, and bike-sharing
  Subsidize or discount transit program
  Encourage telecommuting and condensed work weeks
  Sponsor vanpool/shuttle
  Price workplace parking, or offer employee cash-outs
Bike storage
Locate employment centers and destinations close to transit or improve transit access
Photo credit: (2013). Bay Area Bike Share is now in San Francisco [photograph]. San Francisco Municipal Transportation Authority.
Notes: Background image could be of bike infrastructure? Or business park?

## Slide 61: Transit System Improvements
Fund or operate local shuttles
Improve transit system infrastructure:
  Station enhancements, such as real-time information and improved waiting areas
  Bike/ped access improvements, including bike storage and pedestrian paths
  Park-and-ride lots
Fund new transit infrastructure
  Contribute to the construction of a BRT or rail line
Photo credit: Ginty, C. (2006). LA metro liner with bicycle rack [photograph]. en.wikipedia.

## Slide 62: Rural-Specific
Decrease lot sizes/increase densities within town centers
Add/improve sidewalks, bicycle lanes and racks
Orient buildings toward street
Mix uses
Operate and subsidize vanpools and on-demand shuttles
Photo credit: Crumm, I. (2007). GrassValleyCAHotel [photograph]. en.wikipedia.
Notes: 1. 10-20 acres per unit. This prevents too much growth from occurring in rural areas, channeling it all toward areas that have the accessibility and transit supply to absorb more population

## Slide 63: Edge- and Suburb-Specific
Cluster new developments compactly
Provide sidewalk treatments that facilitate active mode transportation:
  High quality crosswalks
  Bulb outs and pedestrian refuge islands
  Bike lanes and protected cycle tracks
Charge market rate for parking
Require larger employers to offer bike lockers, changing areas, and showers on-site
Encourage telecommuting
Photo credit: (2009). Old Town Pasadena [photograph]. LA Property Solutions.

## Slide 64: Vehicle-Miles Traveled Impacts on the Environment, Human Health, and Fiscal Health

## Slide 65
E N V I R O N M E N T
Transportation tailpipe emissions produce 36.5% of California greenhouse gas emissions
Carbon dioxide, methane, and nitrogen dioxide emissions all increase with VMT
400 million tons of asphalt is produced in the US for roads
Manufacture of each ton produces 570lbs of CO2
Other car automobile emissions (CO, NOx, PM2.5, and ROC) cause damage to human health and agriculture CO2
Photo credit: Morris, D.P. (2008) Exhaust billows out of a car tailpipe January 2, 2008 in San Francisco, California [Photograph]. Getty Images.

## Slide 66
P U B L I C H E A L T H
1.1 deaths and 75 injuries per million vehicle miles traveled in the US (2011)
As VMT rises, physical activity decreases, and obesity, cardiovascular disease, and rates increase
Neighborhoods built to generate lower VMT tend to encourage active transportation by design
Longer commutes are associated with poor physical and mental health
High VMT-type neighborhoods are also associated with poor physical and mental health
Photo credit: Mcnew, D. (2006) The downtown skyline is enveloped in smog shortly before sunset on Nov. 17, 2006 in Los Angeles, California [Photograph]. Getty Images.
Notes: 4. Increased blood pressure and heart rate, negative mood, poor concentration levels, and aggression
5. social isolation, anxiety, increased blood pressure, headaches, stress, and depression

## Slide 67
E N E R G Y
More disperse, high-VMT areas tend to use more energy for heating and cooling.
Typically, a large lot single family home in California uses nearly 3 times as much as a multifamily home
HOUSING TYPE | ANNUAL ENERGY CONSUMPTION (2005)
Large lot single family | 100 million Btu
Small lot single family | 71 million Btu
Attached single family | 54 million Btu
Multifamily | 38 million Btu
Photo credit: Rupert, N. (2008). Chicago Suburbs at night [Photograph].

## Slide 68
W A T E R
High VMT-type developments use more water, mostly due to outdoor use
Typically, a large lot single family home in California uses twice as much as a multifamily home
Higher VMT means more runoff.
HOUSING TYPE | ANNUAL WATER CONSUMPTION (2005)
Large lot single family | 194,000 gal
Small lot single family | 125,000 gal
Attached single family | 93,000 gal
Multifamily | 89,000 gal
Notes: Also in water loss during transport (from pipe leaks)
3. Because more roads need to be built, thus increasing impervious surface land cover. Increasing residential densities from 1 to 8 units can decrease surface runoff by up to 74%

## Slide 69
A G R I C U L T U R E A N D O P E N S P A C E
Higher VMT developments tend to consume more land that would otherwise be used for agriculture
The most compact growth scenarios can save half of all agriculturally sensitive land, and all of wetland areas, while still accommodating the same amount of growth
Photo credit: Urban (2006). Californiacentralvalley [photograph]. en.wikipedia. Permission to reprint by en.wikipedia.
Notes: Because they are more disperse, and occupy more land for the same amount of development (if a community is denser, it is absorbing development demand on a smaller footprint)
From a survey/study of Bay Area + Sacramento Area growth scenarios

## Slide 70
I N C R E A S E D C O S T
T O L O C A L
G O V E R N M E N T
Higher VMT-type developments require higher road construction expenditures
Water and sewer infrastructure expenditures, as well as public service operating costs, reduce when development is more compact
Photo credit: Braut, S. (2008). Los Angeles urban sprawl [Photograph].
Notes: less disperse developments tend to cost 75% compared to more disperse
Water and sewer reduced by 6.6% under compact scenarios. Compact growth scenarios could result in a compounding 2% annual budgetary savings for municipalities—up to $4 billion nationally between 2000 and 2025.

## Slide 71
H O U S I N G S U P P L Y
A N D D E M A N D
M I S M A T C H
The four big California MPOs already suffer from an oversupply of traditional units
1/3 of American households want access to transit yet fewer than 10% have this
Younger generations are already showing a strong preference for Smart Growth communities
Already a near-term deficit in transit-oriented housing
California is not on the path to build enough transit-oriented housing
Photo credit: Laura Segall/Bloomberg via Getty Images.
Notes: 3 million in excess, as of 2012, according to
3. 61% of those born 1979-1996, versus 47% of those born 1934-1950
4. Housing stock increases annually only by 2%, so even if all new California residential units built in California were in transit station areas, the demand would still not be met by 2035
4. 2005-2025 there were 14.6 million households looking to locate within .5 miles of fixed-guideway transit, yet in 2005, there were only 6 million such houses available